## Slide 1: An Autonomous Hydroponic Herb Garden
Group 6: HYDROPONOMOUS
Jessica Cohen
Jamie Collier
Bikesh Dahal
Ben LeBlanc

## Slide 2: Hydroponics Overview
Hydroponics
  Method of growing plant using water based mineral solution, without soil.
Benefits:
  Requires less water.
  Allows for greater control of nutrient levels.
  Easier to keep it pest and disease free.
  Results in healthier plant growth.
Disadvantages:
  Requires more maintenance.

## Slide 3: Objective of the Design
General Objectives:
  Create a fully automated, counter top, hydroponic herb garden.
  Provide consumers with ability to grow herbs in urban living environments easily and cost-effectively.
  Aesthetically pleasing exterior design.
Technical Objectives:
  Automatically monitor and maintain pH, electrical conductivity and temperature of the nutrient solution.
  Feedback control system for nutrients.

## Slide 4: Initial Concept and Final Design
Initial Concept:
  Ebb and Flow
    Grow tray flooded with nutrients and then drained back.
    Timer is set to perform the action multiple times a day.
    Versatile but vulnerable to power outages, pump, and timer failures.
Final Design:
  Nutrient Film Technique (NFT)
    Nutrient solution constantly flows past the roots.
    Reduced volume of nutrient solution required.
    Leading method used for desired plant production.

## Slide 5: Ebb-and-Flow vs. NFT
Ebb-and-Flow
Pros
  Simple fluid dynamics
  Great for small-scale
  Simple construction
Cons
  Water stagnation
  Inefficient water use
  Only provides moderate level of care
NFT
Pros
  Commonly used for herbs
  Self-stirring
  Continuous flow (no timer)
Cons
  Continuous power to pump
  Maintaining nutrient film a challenge (1L/min)
  Overgrown root system may halt flow

## Slide 6: Overview of Literature Review
Internet Search:
  Most of the existing products are manually operated and lack feedback systems for pH, electrical conductivity, temperature and nutrients.
  Few devices have semi automated feedback control systems but are really expensive. ($1,500 or more).
  Examples: Super Box, Aero Pro 7, Water Works, Modern Sprout.
Journal Search:
  Important to monitor and regulate pH, temperature, and electrical conductivity for better growth of plants.

## Slide 7: Control System
Arduino is used as the brain of the control system.
pH:
  Monitor: pH sensor
  Regulate: Administer solution via peristaltic pump
Temperature:
  Monitor: Temperature sensor
  Regulate: Heater operated by mechanical relay
Electrical Conductivity:
  Monitor: EC sensor
  Regulate: Administer solution via peristaltic pump

## Slide 8: CAD Model

## Slide 9: Basic Assumptions for Analysis
Nutrient Solution has same properties as Water
Incompressible
Constant Pressure
Laminar Flow
Dimensions of Reservoir | 
Length (in) | 18.50
Width (in) | 12.00
Height (in) | 3.50
Volume (in^3) | 777.00
Area (in^2) | 222.00
Volume (gal) | 3.36

## Slide 10: Head Loss
Head Loss
  Total less of head of the fluid throughout a pipe
Tubing Specifications | 
Diameter (in) | 0.38
Length (in) | 18.00
Friction | 0.00
Area (in^2) | 0.29
Flow Rate (l/m) | 1.00
Velocity (m/s) | 3.17E-09
Head Loss | 
Hl(m) | 1.23E-22

## Slide 11: Evaporation of Water
Pool Equation
  Evaporation based on the exposed surface area
Evaporation of Water | 
theta (kg/m^2h) | 25.00
Xs (20c) (kg/kg) | 1.47E-02
X (20c) (kg/kg) | 7.00E-03
gh (gal/week) | 1.22
Xs (25c) (kg/kg) | 1.98E-02
X (25c) (kg/kg) | 9.80E-03
gh (gal/week) | 1.59

## Slide 12: Water Usage
Based on evaporation and plant intake
Water Usage in a week | 
Usage (20C) (gal) | 1.77
Usage (25C) (gal) | 2.52
Water left (20C) (gal) | 1.59
Water left (25C) (gal) | 0.85
height (20C) (in) | 1.66
height (25C) (in) | 0.88
Water Intake | 
intake (gal/week) (20C) | 0.55
intake (gal/week) (25C) | 0.92

## Slide 13: Wall Pressure
Water pressure on wall
  Resultant force at 1/3 height
Force on Walls | 
Pave (N/m2) | 436.05
Fmax (N) | 18.22
Fmin (N) | 11.82
Weight (N) | 124.91

## Slide 14: Heating Water
Basic heat transfer equation
Heat Transfer - Heating Water | 
Q (watts) | 100.00
Cp (kJ/kg K) | 4.19
Mass of water (kg) | 12.73
dt (1) | 1.00
Q(kJ) (1) | 53.35
Time (1) min | 8.89

## Slide 15: Nutrient Solution
Dilution of the nutrient Solution
  Conversions
  Dosing
Nutrient Solution | 
Conversion | 1 gal:750 gal
Volume (gal) | 3.36
Water (gal) | 3.36
Nutrients (gal) | 4.48E-03
Volume (liters) | 12.72
Water (liters) | 12.70
Nutrients (liters) | 1.70E-02
pH up/pH down | 
Conversion | 1ml:1gal
pH (ml) | 3.36

## Slide 16: Growing Specifications
Plant Name | Lighting conditions | Lamp Type | Temperature | pH | PPM/TDS
Basil | High Light | T5 | warm | 5.5-6.5 | 700-1120
Mint | High light | T5 | warm | 5.5-6.5 | 1400-1680
Oregano | high light | T5 | warm | 6.0-7.0 | 1120-1400
Parsley | high light | T5 | warm | 5.5-7.0 | 560-1260
Sage | high light | T5 | warm | 5.5-6.5 | 700-1120
Scallion | high light | T5 | warm | 6.0-7.0 | 980-1260
Thyme | high light | T5 | warm | 5.5-7.0 | 560-1120

## Slide 17: Major Purchase Items
Item | Item # | Manufacturer | Price Per Item | # | Total Cost
EC kit (k=0.1) | N/A | Atlas Scientific | $159.95 | 1 | $159.95
Arduino Mega 2560 | MKSP5 | MakerShed | $64.99 | 1 | $64.99
Peristaltic pump | ID: 1150 | adafruit | $24.95 | 3 | $74.85
Serial Conversion Unit | PRT-00449 | SparkFun | $13.95 | 1 | $13.95
SSR 16-channel | SKU:20-018-103 | Sainsmart | $20.99 | 1 | $20.99
Pump | 728490 | Horticulture Source | $6.12 | 1 | $6.12
Air Pump | ASIN: B004PB8SMM | Amazon | $11.04 | 1 | $11.04
Air Bubbler | ASIN: B0050HJ7Q6 | Amazon | $7.84 | 1 | $7.84
Water Heater | ASIN: B00513MZ1I | Amazon | $11.29 | 1 | $11.29
Total Cost: $321.12

## Slide 18: Secondary Purchase Items
Item | Item # | Manufacturer | Price Per Item | # | Total Cost
Arduino Mega Case | ASIN: B00D8J2UK8 | Amazon | $9.99 | 1 | $9.99
Magnets | ASIN: B001KV38ES | Amazon | $7.87 | 1 | $7.87
Grow Light | # 203124380 | Home Depot | $24.97 | 2 | $49.94
Breadboard for Mega | 872-206-0001-01 | Mouser | $13.00 | 1 | $13.00
Tubing | ASIN: B0002563MM | Amazon | $1.37 | 1 | $1.37
Total Cost: $82.17

## Slide 19: Plan
Chart: 
| Finalize CAD | Arduino Coding | Component Delivery | Solution Calibration | Arduino Code Testing | Assembly - Acrylic box | Flow Analysis | Assembly - Electronics | Website Design | Growing Plants/Adjusting | Presentation
Start Date | 41686 | 41686 | 41690 | 41705 | 41700 | 41690 | 41712 | 41714 | 41718 | 41721 | 41723
Duration | 14 | 14 | 14 | 7 | 14 | 27 | 7 | 7 | 14 | 21 | 31

## Slide 20: Risks
System not properly waterproofed
Control system not adequately fine tuned
Power outages
Inconsistent nutrient film
Rapid water loss from evaporation
Grow lights will exceed budget