TECHNOLOGY BRIEF

Title:			Scanless linear and nonlinear laser microscopy

Lead Inventors:	Rafael Yuste, M.D., Ph.D.; Darcy Peterka, Ph.D.;

Volodymyr Nikolenko, Ph.D.; Brendon Watson, Ph.D, M.D.

Tech Ventures Reference:	IR M08-104, IR M08-107

# Problem or Unmet Need

Laser scanning microscopy generally offers excellent spatial resolution, but poor temporal resolution. The current approach is to either scan the observed region pixel-by-pixel, requiring relatively long acquisition times, or to split the beam using amplitude modulators, limiting the total amount of light energy that can be transmitted to the sample. Reduced energy output is particularly significant for nonlinear microscopies, such as two-photon fluorescence, which require high peak energies for efficient excitation. In two-photon microscopy, two low energy photons can be absorbed simultaneously, exciting the fluorophore, and generally results in better signal-to-noise, increased sample penetration, and reduced photodamage, all of which are crucially important for imaging or photostimulating live tissue. Because excitation requires near coincident absorption of two photons, high instantaneous light fluxes are critical. Therefore, amplitude-based beam splitters that simply remove light from regions that are not supposed to be illuminated typically do not help in two-photon applications.

# Details of the Invention

This technology allows for high-speed, multi-region scanning that can utilize the full energy of a laser. By using a diffractive spatial light modulator (SLM), a laser can be rapidly focused into multiple beamlets without any moving parts. Because the SLM uses phase modulation rather than amplitude ‘filtering’, the laser’s total energy is effectively redistributed into the desired spatial pattern with minimal loss. The invention consists of methods for using an SLM to manipulate laser sources in microscopy and software for easy and rapid specification of targeted regions. In addition, the inventors demonstrate a novel strategy for fast imaging using specific scanless illumination of selected locations by utilizing a wide-field detector.

Indeed, an SLM microscope could be viewed as the ultimate “optics” since it can mimic most optical transfer functions of conventional microscopes, for example focusing of light or optically zooming into a sample, but without any moving parts. It is conceivable that SLM microscopy could replace in software many of the functions that current microscopes carry out in hardware.

The technology has been implemented in two types of fully functional prototypes:

- As part of a standard microscope ‘add-on’ unit. This device can be quickly and easily adapted to existing commercial microscopes.

- As a stand-alone portable microscope fully-capable of targeted imaging and photostimulation. Some further miniaturization could also allow for in vivo imaging/photostimulation applications or medical use of the device in the field.

# Applications:

- High speed imaging of multiple regions of interest (ROIs) – highly useful for live cell imaging techniques, such as calcium- or voltage-sensitive dyes

- Photostimulation / Photodynamic therapy – excitation can be precisely targeted and rapidly modulated to multiple points (‘caged’ compounds, optogenetics, etc.)

- Active correction of optical aberrations in existing optical systems

- iso-STED and other super-resolution imaging modalities

# Advantages:

- No moving parts – multiple targets can be imaged (or excited) at millisecond rates; minimal risk of mechanical failure; reduced up-front and maintenance costs

- Higher power delivered to multiple targets – allows for use in two-photon applications or other linear or non-linear imaging / photostimulation modalities

  - Photostimulation can be much more precisely targeted

  - Reduced photodamage to non-target regions compared to conventional laser scanning

- Small size – portable units; in vivo applications

Patent Status:	Patent Pending (WO/2010/036972)

Licensing Status:	Available for Licensing or Sponsored Research Support

Publications:	Press Release: A Bright Idea for a New Kind of Microscope

Howard Hughes Medical Institute (HHMI), December 19, 2008

SLM Microscopy: Scanless Two-Photon Imaging and Photostimulation with Spatial Light Modulators. Nikolenko V, Watson BO, Araya R, Woodruff A, Peterka DS, Yuste R. Front Neural Circuits. 2008;2:5. Epub 2008 Dec 19.

Comment in:

A new phase for two-photon microscopy

Timothy E. Holy, Frontiers in Neuroscience. 2009

A portable laser photostimulation and imaging microscope. Nikolenko V, Peterka DS, Yuste R. Journal of Neural Engineering 2010 Aug;7(4):045001. Epub 2010 Jul 19.

Two-photon imaging with diffractive optical elements.

Watson BO, Nikolenko V, Yuste R. Front Neural Circuits. 2009;3:6.

Two-photon photostimulation and imaging of neural circuits. Nikolenko V, Poskanzer KE, Yuste R. Nature Meth. 2007 Nov;4(11):943-50.

Website: http://www.twophoton.com

Further Information:	Columbia | Technology Ventures

Beth Kauderer, J.D., Ph.D.; Tel: (212) 854-4941

Email: TechTransfer@columbia.edu